## Slide 1
Chapter 3 and Appendix C
Cache Optimization Techniques
Computer Architecture
A Quantitative Approach

## Slide 2: CACHE OPTIMIZATION TECHNIQUES - APPENDIX C / CHAPTER 3
(Part 2)

## Slide 3: Outline
ILP
Compiler techniques to increase ILP
Loop Unrolling
Static Branch Prediction
Dynamic Branch Prediction
Overcoming Data Hazards with Dynamic Scheduling
Tomasulo Algorithm
Conclusion

## Slide 4: Recall from Pipelining
Pipeline CPI =
Ideal pipeline CPI
+ Structural Stalls
+ Data Hazard Stalls
+ Control Stalls
Ideal pipeline CPI: measure of the maximum performance attainable by the implementation
Structural hazards: HW cannot support this combination of instructions
Data hazards: Instruction depends on result of prior instruction still in the pipeline
Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps)

## Slide 5: Instruction Level Parallelism
Instruction-Level Parallelism (ILP): overlap the execution of instructions to improve performance
2 approaches to exploit ILP:
  Rely on hardware to help discover and exploit the parallelism dynamically (e.g., Pentium 4/core2/i3/i5/i7, AMD Opteron, IBM Power)
  Rely on software technology to find parallelism, statically at compile-time (e.g., Itanium 2/IA-64)

## Slide 6: Instruction-Level Parallelism (ILP)
Basic Block (BB) ILP is quite small
  BB: a straight-line code sequence with NO branches in except to the entry and no branches out except at the exit
  Average dynamic branch frequency 15% to 25%
=> 4 to 7 instructions execute between a pair of branches
  Plus, instructions in BB likely to depend on each other
Need ILP across multiple BBs
Simplest: loop-level parallelism to exploit parallelism among iterations of a loop.
For example,
for (i=1; i<=1000; i=i+1) x[i] = x[i] + y[i];

## Slide 7: Loop-Level Parallelism
Exploit loop-level parallelism by “unrolling loop” either by
  Dynamic via branch prediction or
  Static via loop unrolling by compiler
Determining dependences critical
If 2 instructions are
  Parallel, they can execute simultaneously in a pipeline of arbitrary depth without causing any stalls (assuming no structural hazards)
  Dependent, they are not parallel and must be executed in order, although they may often be partially overlapped

## Slide 8: Data Dependence and Hazards
InstrJ is data dependent (aka true dependence) on InstrI:
  InstrJ tries to read operand before InstrI writes it
I: add r1,r2,r3 J: sub r4,r1,r3
  or InstrJ is data dependent on InstrK which is dependent on InstrI
If two instructions are data dependent, they cannot execute simultaneously or be completely overlapped
Data dependence in instruction sequence
 data dependence in source code
 effect of original data dependence must be preserved
If true data dependence caused a hazard in pipeline, that’s a Read After Write (RAW) hazard

## Slide 9: ILP and Data Dependencies, Hazards
HW/SW must preserve the illusion of program order: order instructions would execute in, when executed sequentially as determined by original source program
  Dependences are a property of programs
Presence of dependence indicates potential for a hazard
  But hazard and length of any stall is property of the pipeline
Importance of the data dependencies
  indicates the possibility of a hazard
  determines order in which results must be calculated
  sets an upper bound on how much parallelism can possibly be exploited
HW / SW goal: exploit parallelism by preserving program order only where it affects the outcome of the program
Notes: …
However, actual hazard and length of any stall is property of the pipeline

## Slide 10: Name Dependence #1: Anti-dependence
Name dependence
– When 2 instructions use same register or memory location, called a name, but no flow of data between the instructions associated with that name; 2 versions of name dependence
InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”
If anti-dependence caused a hazard in the pipeline, that’s a Write After Read (WAR) hazard
I: | sub | r4,r1,r3
J: | add | r1,r2,r3
K: | mul | r6,r1,r7

## Slide 11: Name Dependence #2: Output dependence
InstrJ writes operand before InstrI writes it.
Called an output dependence by compiler writers. This also results from the reuse of name “r1”
If output-dependence caused a hazard in the pipeline, that’s a Write After Write (WAW) hazard
Instructions involved in a name dependence could execute simultaneously if name used in instructions is changed so instructions do not conflict
  Register renaming resolves name dependence for registers
  Either by compiler or by HW
I: | sub | r1,r4,r3
J: | add | r1,r2,r3
K: | mul | r6,r1,r7

## Slide 12: Control Dependencies
Every instruction is control dependent on some set of branches, and, in general, these control dependencies must be preserved to preserve program order
if p1 { S1;
}
if p2 { S2;
}
S1 is control dependent on p1, and S2 is control dependent on p2 but not on p1.

## Slide 13: Review Question
Assume a machine has a 6-stage pipeline
  The branch direction and target are known in the 5th stage
  20% of instructions are branches on average
  Branch is statically predicted as not-taken
  60% correct prediction on average
How many cycles are wasted per branch misprediction on this machine?
A. 3
B. 4
C. 5
D. 6
Notes: >>
The number of cycles wasted per branch misprediction is
determined by the number of pipeline stages between
the point where the branch outcome is known
and the point where the prediction is made.
In this case,
the branch direction and target are known in the 5th stage of the 6-stage pipeline,
meaning the prediction is resolved in stage 5.
Since branch prediction occurs during the fetch stage (stage 1),
the misprediction penalty is the number of stages from the fetch stage
to the stage where the branch is resolved, which is 5 - 1 = 4 stages.
So, B. is the answer.

## Slide 14
Assume a machine has a 6-stage pipeline
  The branch direction and target are known in the 5th stage
  20% of instructions are branches on average
  Branch is statically predicted as not-taken
  60% correct prediction on average
What is the average CPI after the control stalls are considered? Assume that there is no other stalls, and the ideal CPI is 1.
Review Question
Notes: >>
Average CPI = Ideal CPI + Branch Frequency * (1 – Prediction Accuracy) * Penalty
Average CPI = 1 + 0.2 * 0.4 x 4 = 1 + 0.32 = 1.32

## Slide 15: Violating Control Dependence
2 properties critical to program correctness are
  exception behavior and
  data flow
By preserving the control and data dependences, we can keep correct exception behavior and data flow
Control dependence need not be preserved, if we can do so without affecting correctness of the program
– willing to execute instructions that should not have been executed, thereby violating the control dependence

## Slide 16: Exception Behavior
Preserving exception behavior means:
  any changes in instruction execution order must not change how exceptions are raised in the program (no new exceptions)
  Example:
No dependence between BEQZ and LW – both read R2.
But LW execution is control dependent on BEQZ
What if we switch the execution order of the two to achieve performance improvement?
» If the branch is not taken, a potential stall for the use of the value loaded by LW would be saved.
Problem with executing LW before BEQZ?
R2,L1
R1,0(R2)
DADDU R2,R3,R4 BEQZ
LW
L1:
Assume no branch delay slot

## Slide 17: Data Flow
Data flow: actual flow of data values among instructions that produce results and those that consume them
– branches make flow dynamic, determine which instruction is the supplier of data
Example:
OR uses on R1 from DADDU or DSUBU?
Must preserve data flow on execution
– Preserving the control dependence prevents illegal change to the flow
DADDU R1,R2,R3 BEQZ R4,L DSUBU R1,R5,R6
L: … OR
R7,R1,R8
Assume no branch delay slot

## Slide 18: Software Techniques - Example
This code, add a scalar to a vector:
for (i=1000; i>=0; i=i–1) x[i] = x[i] + s;
Assume following latencies for all examples
– Ignore delayed branch in these examples
Instruction between producing result | Instruction using result | stalls in cycles
FP ALU op FP ALU op Load double Load double Integer op | Another FP ALU op Store double FP ALU op Store double Integer op | 3 2 1 0 0

## Slide 19: FP Loop: Where are the Hazards?
First translate into MIPS code:
R1 has the address of the last array element
F2 has the scalar value
R2 has the start address of array
for (i=1000; i>=0; i=i–1) x[i] = x[i] + s;
Loop: L.D | F0,0(R1) | ;F0=vector element
ADD.D | F4,F0,F2 | ;add scalar from F2
S.D | F4, 0(R1) | ;store result
DADDUI | R1,R1,-8 | ;decrement pointer 8B (DW)
BNE
R1,R2,Loop;branch R1!=R2

## Slide 20: FP Loop Showing Stalls
9 clock cycles: Rewrite code to minimize stalls?
for (i=1000; i>=0; i=i–1) x[i] = x[i] + s;
1 Loop: | L.D | F0,0(R1) | F0,0(R1) | ; | F0=vector element |  | 
2 | stall |  |  |  |  |  | 
3 | ADD.D | F4,F0,F2 | F4,F0,F2 | ; | add scalar in F2 |  | 
4 | stall |  |  |  |  |  | 
5 | stall |  |  |  |  |  | 
6 | S.D | F4,0(R1) | F4,0(R1) | ; | store result |  | 
7 | DADDUI | R1,R1,-8 | R1,R1,-8 | ; | decrement pointer 8B (DW) |  | 
8 | stall |  |  | ; | can’t forward to branch ID |  | 
9 | BNE | R1,R2,Loop | R1,R2,Loop | ; | branch R1!=zero |  | 
plus branch delay! |  |  |  |  |  |  | 
Instruction producing result |  | Instruction using result |  |  |  |  | Latency in clock cycles
FP ALU op |  | Another FP ALU |  |  |  | op | 3
FP ALU op |  | Store double |  |  |  |  | 2
Load double |  | FP ALU op |  |  |  |  | 1

## Slide 21: Revised FP Loop Minimizing Stalls
7 clock cycles, but just 3 for execution (L.D, ADD.D,S.D), 4 for loop overhead; How make faster?
Instruction producing result | Instruction using result |  | Latency in clock cycles
FP ALU op | Another FP ALU | op | 3
FP ALU op | Store double |  | 2
Load double | FP ALU op |  | 1
1 Loop: 2 | L.D DADDUI | F0,0(R1) R1,R1,-8 ; moved to here | 
3 | ADD.D | F4,F0,F2 | 
4 | stall |  | 
5 | stall |  | 
6 | S.D | F4,8(R1) ;altered offset when move | DSUBUI
7 | BNE | R1,R2,Loop | 
DADDUI first, then S.D (address change is needed)

## Slide 22: Unroll Loop Four Times (straightforward way)
Rewrite loop to minimize stalls?
1 Loop:L.D F0,0(R1)
3 ADD.D F4,F0,F2
6 S.D F4,0(R1)
cycle stall
cycles stall
;drop DADDUI & BNE
7 | L.D F6,-8(R1) |  |  |  | 
9 | ADD.D F8,F6,F2 |  |  |  | 
12 | S.D F8,-8(R1) | ;drop | DADDUI | & | BNE
13 | L.D F10,-16(R1) |  |  |  | 
15 | ADD.D F12,F10,F2 |  |  |  | 
18 | S.D F12,-16(R1) | ;drop | DADDUI | & | BNE
19 | L.D F14,-24(R1) |  |  |  | 
21 | ADD.D F16,F14,F2 |  |  |  | 
24 | S.D F16,-24(R1) |  |  |  | 
25 | DADDUI R1,R1,-32 | ;alter | to 4*8 |  | 
27 | BNE R1,R2,LOOP |  |  |  | 
27 clock cycles, or 6.75 per iteration
(Assumes R1 is multiple of 4)
Notes: 3.2

## Slide 23: Unrolled Loop That Minimizes Stalls
1 | Loop: | L.D | F0,0(R1) | 
2 |  | L.D | F6,-8(R1) | 
3 |  | L.D | F10,-16(R1) | 
4 |  | L.D | F14,-24(R1) | 
5 |  | ADD.D | F4,F0,F2 | 
6 |  | ADD.D | F8,F6,F2 | 
7 |  | ADD.D | F12,F10,F2 | 
8 |  | ADD.D | F16,F14,F2 | 
9 |  | S.D | F4,0(R1) | 
10 |  | S.D | F8,-8(R1) | 
11 |  | S.D | F12,-16(R1) | 
12 |  | DADDUI | R1,R1,-32 | 
13 |  | BNE | R1,R2,LOOP | 
14 |  | S.D | F16, 8(R1) ; | delay slot
14 clock cycles, or 3.5 per iteration Assume that branch is resolved in ID

## Slide 24: Unrolled Loop Detail
Do not usually know upper bound of loop
Suppose it is n, and we would like to unroll the loop to make k copies of the body
Instead of a single unrolled loop, we generate a pair of consecutive loops:
  1st executes (n mod k) times and has a body that is the original loop
  2nd is the unrolled body surrounded by an outer loop that iterates (n/k) times
For large values of n, most of the execution time will be spent in the unrolled loop

## Slide 25: 5 Loop Unrolling Decisions
Requires understanding how one instruction depends on another and how the instructions can be changed or reordered given the dependences:
Determine loop unrolling useful by finding that loop iterations were
independent (except for maintenance code)
Use different registers to avoid unnecessary constraints forced by using same registers for different computations
Eliminate the extra test and branch instructions and adjust the loop termination and iteration code
Determine that loads and stores in unrolled loop can be interchanged by observing that loads and stores from different iterations are independent
– Transformation requires analyzing memory addresses and finding that they do not refer to the same address
Schedule the code, preserving any dependences needed to yield the same result as the original code

## Slide 26: 3 Limits to Loop Unrolling
Decrease in amount of overhead amortized with each extra unrolling
  Amdahl’s Law
Growth in code size
  For larger loops, concern it increases the instruction cache miss rate
Register pressure: potential shortfall in registers created by aggressive unrolling and scheduling
  If not possible to allocate all live values to registers, may lose some or all of its advantage
Loop unrolling reduces impact of branches on pipeline; another way is branch prediction