## Slide 1
Chapter 3 and Appendix C
Tomasulo’s Algorithm
Computer Architecture
A Quantitative Approach
Notes: >>
Instruction reordering vs. Dynamic scheduling:
Instruction reordering, loop merge, loop interchange, loop fusion, and loop unrolling are all
techniques used in compiler optimization to improve program performance
by altering the structure or execution order of code, particularly within loops.
(limited to a static view of the program and cannot adapt to runtime conditions)
Dynamic scheduling, on the other hand, is a hardware-based technique
that allows the processor to reorder instruction execution at runtime based on data availability and resource status.
(allows the processor to respond to unpredictable events
like cache misses or branch mispredictions
by executing other ready instructions)

## Slide 2: Outline
ILP
Compiler techniques to increase ILP
Loop Unrolling
Static Branch Prediction
Dynamic Branch Prediction
Overcoming Data Hazards with Dynamic Scheduling
(Start) Tomasulo Algorithm
Conclusion

## Slide 3: Advantages of Dynamic Scheduling
Dynamic scheduling - hardware rearranges the instruction execution to reduce stalls while maintaining data flow and exception behavior (out-of-order execution)
It handles cases in which dependences were unknown at compile time
– Allows the processor to tolerate unpredictable delays (e.g., cache misses), by executing other code while waiting for the miss to resolve
It simplifies the compiler
It allows code compiled for one pipeline to run efficiently on a different pipeline
Hardware speculation, a technique with significant performance advantages, builds on dynamic scheduling
Notes: >>
Advantages of Dynamic Scheduling:
1. Hardware dynamically rearranges instruction execution (out-of-order execution) to reduce stalls.
(arrow down)
2. Handles unknown compile-time dependences and tolerates unpredictable delays (e.g., cache misses).
(arrow down)
3. Simplifies the compiler, allows portable compilations, and enables hardware speculation.

## Slide 4: HW Schemes: Instruction Parallelism
Key idea: Allow instructions behind stall to proceed
DIV.D ADD.D SUB.D
F0,F2,F4 F10,F0,F8 F12,F8,F14
Enables out-of-order execution and allows out-of-order completion (e.g., SUBD before slow DIVD)
– In a dynamically scheduled pipeline, all instructions still pass through issue stage in order (in-order issue)
Will distinguish when an instruction begins execution from when it completes execution; between the two times, the instruction is in execution
Note: Dynamic scheduling creates WAR and WAW hazards, and makes exception handling harder
Notes: >>
Key idea:
Allow instructions behind a stall to proceed,
which enables out-of-order execution
and allows out of-order completion.
(arrow down)
Instructions are still issued in-order.
(arrow down)
Instruction pipelining is still tracked during a long running execution.
(arrow down)
Note:
However, dynamic scheduling creates
WAR (Write-After-Read) and
WAW (Write-After-Write) hazards,
complicating exception handling.

## Slide 5: HW Schemes: Instruction Parallelism
DIV.D ADD.D
SUB.D MUL.D
F0,F2,F4 F6,F0,F8
F8,F10,F14 F6,F10,F8
Existence of anti- & output dependence. An example:
Anti-dependence?
Output dependence?
True dependence?
Notes: >>
Here is an example to illustrate the
existence of anti-, output, and true dependences.

## Slide 6: HW Schemes: Instruction Parallelism
Existence of anti- & output dependence. An example:
DIV.D ADD.D
SUB.D MUL.D
F0,F2,F4 F6,F0,F8
F8,F10,F14 F6,F10,F8
Anti-dependence?
» Between ADD.D and SUB.D
» SUB.D may complete while ADD.D is waiting - WAR hazard
Output dependence?
» Between ADD.D and MUL.D
» MUL.D may complete while ADD.D is waiting - WAW hazard
True dependence?
» Between DIV.D and ADD.D
Notes: >>
Anti-dependence (WAR):
Between ADD.D and SUB.D (on F8).
Output dependence (WAW):
Between ADD.D and MUL.D (on F6).
True dependence (RAW):
Between DIV.D and ADD.D (on F0).

## Slide 7: Dynamic Scheduling - Step 1
Simple pipeline had only one stage to check both structural and data hazards: Instruction Decode (ID), also called Instruction Issue
Dynamic scheduling hardware splits the ID pipe stage of simple 5-stage pipeline into 2 stages to make a 6-stage pipeline:
  Issue—Decode instructions, check for structural hazards
  Read operands—Wait until no data hazards, then read operands
  Recall Scoreboard method
Notes: >>
Recall the basic 5-stage pipeline checked for both structural and data hazards in the instruction decode stage.
(arrow down)
Dynamic scheduling hardware splits the
Instruction Decode (ID) pipeline stage into two:
Issue (decode, check structural hazards) and
Read Operands (wait for no data hazards, then read).

## Slide 8: A Dynamic Algorithm: Tomasulo’s
For IBM 360/91 (before caches!)
 long memory latency and FP delays
Goal: Achieve high floating-point performance for entire 360 family, without special compilers
Small number of floating-point registers (4 in IBM 360) prevented interesting compiler scheduling of operations
  This led Tomasulo to try to figure out how effectively to get more registers — renaming in hardware!
Why Study a 1966 Computer?
The descendants of this have flourished!
  Alpha 21264, Pentium 4, AMD Opteron, Power 5, …
Notes: >>
Tomasulo’s algorithm was invented for the IBM 360/91 (in 1966) due to long latencies and floating-point delays.
(arrow down)
Main innovation:
Uses register renaming in hardware to overcome the small number of physical registers.
(arrow down)
Q. So why do we study a computer from 1966?
(arrow down)
A. Descendants are used in modern CPUs (e.g., Pentium 4, Alpha 21264).

## Slide 9: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations (RSs); called register renaming
  Renaming avoids WAR, WAW hazards
  More RSs than registers, so can do optimizations compilers cannot
Results to FU from RS, not through registers, but over a Common Data Bus (CDB) that broadcasts results to register file, awaiting RSs, and store buffers
  Avoids RAW hazards by executing an instruction only when its operands are available
Load and Stores are treated as FUs with RSs as well
Integer instructions can go past branches (predict taken), also allow FP ops beyond basic block in FP queue
Notes: >>
The control and buffers are distributed with Functional Units (FU).
(arrow down)
Buffers are called Reservation Stations (RSs).
Register renaming avoids WAR and WAW hazards.
(arrow down)
Results are broadcast on the Common Data Bus (CDB),
which avoids RAW hazards by executing instructions only when operands are available.
(arrow down)
Loads/Stores are scheduled as functional units using reservation stations.
(arrow down)
Execution aggressively proceeds past branches using prediction,
allowing both integer and Floating-Point (FP) instructions to be issued speculatively.

## Slide 10: Tomasulo Organization
FP adders
Add1 Add2 Add3
FP multipliers
Mult1 Mult2
From Mem
FP Registers
Reservation Stations
Common Data Bus (CDB)
To Mem
FP Ops Queue
Load Buffers
Store Buffers
Load1 Load2 Load3 Load4 Load5 Load6
Store1 Store2 Store3
Notes: >>
This figure shows the block diagram including
FP Adders,
FP Multipliers,
Load/Store Buffers,
Reservation Stations,
FP Registers,
and the Common Data Bus (CDB)

## Slide 11: Three Stages of Tomasulo Algorithm
Issue - get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instruction & sends operands (renames registers).
Execute - operate on operands (EX)
  Start execution when both operands ready; if not, watch CDB for result
Write result - finish execution (WB)
  Write on CDB to all awaiting units; mark RS available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Completion latencies for instructions in following example slides: 1cc for L.D 2cc for FP ADD (+,-) 10cc for FP MUL 40cc for FP DIV
Notes: >>
Three Stages of Tomasulo Algorithm
Issue: Decode and issue instruction if a Reservation Station (RS) is free (structural hazard check) and perform register renaming. (arrow down)
Execute (EX): Start when both operands are ready. Otherwise, monitor the CDB. (arrow down)
Write Result (WB): Broadcast result on CDB and mark the RS as available
(arrow down)
The architecture differentiates between a standard Normal Data Bus (where data specifies the destination)
and the specialized Common Data Bus (CDB), where data specifies the source.
The CDB is a 68-bit broadcast channel (64 bits of data + 4 bits for the Functional Unit source address).
Units watching the CDB only write the result if the source address matches the one they are waiting for.
(arrow down)
Here are the execution completion latencies for following example:
1cc for LD
2cc for FP ADD (+,-)
10cc for FP MUL
40cc for FP DIV

## Slide 12: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of source operands for Op
  Each store buffer has a V field, for the result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
  Store buffers have only one Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Time: After FU starts EX, number of cycles yet to do
Register result status - Indicates which functional unit will write each register, if one exists. Blank when no pending instructions will write that register.
Notes: >>
Components of a Reservation Station are:
Op: The operation to be perform.
Vj, Vk: Values of source operands.
Qj, Qk: Reservation stations that will produce the source operands (0 if ready).
Busy: Indicates reservation station or FU is busy.
Time: A countdown until the execution is complete.
Register Result Status table tracks which FU is writing to each register.

## Slide 13: Tomasulo Example
Instruction status:
Instruction LD
LD
MULTD SUBD DIVD ADDD
j k
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
Instruction stream
Exec Write
Issue Comp Result
Busy
Address
Load1 No
Load2 No
Load3 No
Reservation Stations:
Busy Op
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Mult1 Mult2
Time Name
Add1 No
Add2 No
No No No
Register result status:
Clock
0
Clock cycle counter
F0 F2 F4 F6 F8 F10 F12 ... F30
FU
FU countdown Add3
3 Load/Buffers
3 FP Adder R.S. 2 FP Mult R.S.
EX
Cycle instruction EXecution starts
1cc for L.D
2cc for FP ADD (+,-)
10cc for FP MUL
40cc for FP DIV
Notes: >>
Here is a step-by-step example execution demonstrating
in-order issue,
out-of-order execution start,
and out-of-order completion
using the three stages.
(Explain the example diagram.)

## Slide 14: Tomasulo Example Cycle 1
Exec
Write
Instruction |  | j | k | Issue | Comp Result |  | Busy | Address
LD | F6 | 34+ | R2 | 1 |  | Load1 | Yes | 34+R2
LD | F2 | 45+ | R3 |  |  | Load2 | No | 
MULTD | F0 | F2 | F4 |  |  | Load3 | No | 
SUBD | F8 | F6 | F2 |  |  |  |  | 
DIVD | F10 | F0 | F6 |  |  |  |  | 
ADDD | F6 | F8 | F2 |  |  |  |  | 
Reservation Stations:
Time
Busy Op
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Name
Add1 No
Add2 No
Add3 No
Mult1 No
Mult2 No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
1 | FU |  |  |  | Load1 |  |  | 
Instruction status:
EX

## Slide 15: Tomasulo Example Cycle 2
Instruction status:
Exec
Write
EX Instruction |  | j | k | Issue | Comp Result |  | Busy | Address
2 LD | F6 | 34+ | R2 | 1 |  | Load1 | Yes | 34+R2
LD | F2 | 45+ | R3 | 2 |  | Load2 | Yes | 45+R3
MULTD | F0 | F2 | F4 |  |  | Load3 | No | 
SUBD | F8 | F6 | F2 |  |  |  |  | 
DIVD | F10 | F0 | F6 |  |  |  |  | 
ADDD | F6 | F8 | F2 |  |  |  |  | 
Reservation Stations:
Time
Busy Op
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Name
Add1 No
Add2 No
Add3 No
Mult1 No
Mult2 No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
2 | FU |  | Load2 |  | Load1 |  |  | 
Note: Can have multiple loads outstanding
Notes: Note:
The load buffers can support multiple outstanding load instructions.

## Slide 16: Tomasulo Example Cycle 3
Instruction status:
Exec
Write
EX Instruction |  | j | k | Issue | Comp Result |  | Busy | Address
2 LD | F6 | 34+ | R2 | 1 | 3 | Load1 | Yes | 34+R2
3 LD | F2 | 45+ | R3 | 2 |  | Load2 | Yes | 45+R3
MULTD | F0 | F2 | F4 | 3 |  | Load3 | No | 
SUBD | F8 | F6 | F2 |  |  |  |  | 
DIVD | F10 | F0 | F6 |  |  |  |  | 
ADDD | F6 | F8 | F2 |  |  |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
R(F4) Load2
Name Busy Op
Add1 No
Add2 No
Add3 No
Mult1 Yes MULTD
Mult2 No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
3 | FU | Mult1 | Load2 |  | Load1 |  |  | 
Note: register names are removed (“renamed”) in RSs; MULTD issued;
Load1 completing; what is waiting for Load1?
Notes: Note:
Register names are removed (“renamed”) in RSs
MULTD issued
Load1 completing execution
Q. What is waiting for Load1?
A. No FUs. (instruction stream has not issued SUBD yet)
However, RAW: SUBD and DIVD.

## Slide 17: Tomasulo Example Cycle 4
Instruction status:
j k
LD F6 34+ R2
LD F2 45+ R3
MULTD F0 F2 F4 SUBD F8 F6 F2 DIVD F10 F0 F6 ADDD F6 F8 F2
EX Instruction
Issue
Exec Write Comp Result
3 4
4
Busy
Address
1
2
3
4
45+R3
Load1 No
Load2 Yes
Load3 No
Reservation Stations:
Time
Name Add1 Add2 Add3 Mult1 Mult2
Busy Op
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Load2
Yes SUBD M(A1)
No
No
Yes MULTD R(F4) Load2
No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
4 | FU | Mult1 | Load2 |  | M(A1) | Add1 |  | 
Load2 completing; what is waiting for Load2?
2
3
Notes: Load2 completing execution
Q. What is waiting for Load2?
A. Add1 (SUBD)
RAW: ADD.D
M(A1): books notation (nonstandard)
Indicates that the source operand will come from a
Load instruction that is currently waiting in Load Buffer A1 (or Load1).

## Slide 18: Tomasulo Example Cycle 5
Instruction status:
Exec Write Issue Comp Result
j k
LD F6 34+ R2
LD F2 45+ R3
MULTD F0 F2 F4 SUBD F8 F6 F2 DIVD F10 F0 F6 ADDD F6 F8 F2
EX Instruction
Busy
Address
3
4
4
5
1
2
3
4
5
Load1 No
Load2 No
Load3 No
Reservation Stations:
Time Name
Busy Op
S1
Vj
S2
Vk
RS
Qj
RS
Qk
2 Add1 Add2
Yes SUBD M(A1) M(A2)
No
No
Add3
Yes MULTD M(A2) Yes DIVD
R(F4)
M(A1)
Mult1
Register result status:
Clock
5
F8 F10 F12 ... F30
F0 F2 F4 F6
FU Mult1 M(A2) M(A1)
Add1
Mult2
FU latency
countdown 10 Mult1
Mult2
Timer starts down for Add1, Mult1
2
3
5
5
Notes: Timer starts counting down for Add1, Mult1
M(A2): books notation (nonstandard)
Indicates that the source operand will come from a
Load instruction that is currently waiting in Load Buffer A2 (or Load2).

## Slide 19: Tomasulo Example Cycle 6
Instruction status:
Exec Write Issue Comp Result
j k
LD F6 34+ R2
LD F2 45+ R3
MULTD F0 F2 F4 SUBD F8 F6 F2 DIVD F10 F0 F6 ADDD F6 F8 F2
EX Instruction
Busy
Address
3
4
4
5
1
2
3
4
5
6
Load1 No
Load2 No
Load3 No
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time Name
1 Add1 Add2 Add3
9 Mult1
Mult2
Busy Op
M(A1) M(A2)
M(A2)
Add1
Yes SUBD Yes ADDD
No
Yes MULTD M(A2) Yes DIVD
R(F4)
M(A1)
Mult1
Register result status:
Clock
6
F0 F2 F4 F6 F8 F10 F12 ... F30
FU Mult1 M(A2) Add2 Add1 Mult2
2
3
5
5
Issue ADD.D despite name output-dependency on F6?
Notes: Q. Issue ADD.D despite name output-dependency on F6?
A. Register renaming addresses WAW.

## Slide 20: Tomasulo Example Cycle 7
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 |  | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 |  | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 |  | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 |  |  |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  |  | 
 | ADDD | F6 | F8 | F2 | 6 |  |  |  |  |  | 
Reservation Stations: |  |  |  |  |  | S1 | S2 | RS | RS |  | 
Time Name |  |  |  | Busy | Op | Vj | Vk | Qj | Qk |  | 
0 Add1 |  |  |  | Yes | SUBD | M(A1) | M(A2) |  |  |  | 
Add2 |  |  |  | Yes | ADDD |  | M(A2) | Add1 |  |  | 
Add3 |  |  |  | No |  |  |  |  |  |  | 
8 Mult1 |  |  |  | Yes | MULTD | M(A2) | R(F4) |  |  |  | 
Mult2 |  |  |  | Yes | DIVD |  | M(A1) | Mult1 |  |  | 
Register result status: |  |  |  |  |  |  |  |  |  |  | 
Clock |  |  |  |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
7 |  | FU |  |  | Mult1 | M(A2) |  | Add2 | Add1 | Mult2 | 
Add1 (SUBD) completing; what is waiting for it?
Notes: Add1 (SUB.D) completing execution
(EX 6-7 due to Load2 WR CDB in 5 for RAW on F2)
Q. What is waiting for it?
A. Add2 (ADD.D)

## Slide 21: Tomasulo Example Cycle 8
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 |  |  |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Busy Op
ADDD (M-M) M(A2)
Time Name
Add1 No Yes No
2 Add2 Add3
7 Mult1
Mult2
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
8 | FU | Mult1 | M(A2) |  | Add2 | (M-M) | Mult2 | 
Notes: (M-M): books notation (nonstandard)
M-M: memory FP, memory FP subtraction
computed value that arrived via the CDB

## Slide 22: Tomasulo Example Cycle 9
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 |  |  |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Busy Op
ADDD (M-M) M(A2)
Time Name
Add1 No Yes No
1 Add2 Add3
6 Mult1
Mult2
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
9 | FU | Mult1 | M(A2) |  | Add2 | (M-M) | Mult2 | 

## Slide 23: Tomasulo Example Cycle 10
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 |  |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Busy Op
ADDD (M-M) M(A2)
Time Name
Add1 No Yes No
0 Add2 Add3
5 Mult1
Mult2
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
10 | FU | Mult1 | M(A2) |  | Add2 | (M-M) | Mult2 | 
Add2 (ADD.D) completing; what is waiting for it?
Notes: Add2 (ADD.D) completing execution.
(EX 9-10 due to Add1 (SUB.D) WR CDB in 8 for RAW on F8)
Q. What is waiting for it?
A. Nothing.
However, WAR exists between DIV.D and ADD.D on F6

## Slide 24: Tomasulo Example Cycle 11
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8
 | DIVD | F10 | F0 | F6 | 5 |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
If scoreboard, ADD.D cannot write result due to F6 read at DIVD (avoid WAR hazard)
RS
Qk
Time
Name Add1 Add2 Add3
Busy Op
No No
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
F0 F2 F4 F6
4 Mult1 Mult2
F8 F10
F12 ... F30
Register result status:
Clock
11
FU Mult1 M(A2) (M-M+M(M-M) Mult2
Write result of ADD.D here?
All quick instructions complete in this cycle!
Notes: However, WAR exists between DIV.D and ADD.D on F6
Q. Write result of ADD.D here?
A. Use register renaming to allow ADD.D to WR.
All quick instructions complete in this cycle! (i.e., LD, SUBD, ADD.D)
(M-M+M): book notation (nonstandard)
M: Stands for a Memory access or Floating-Point Value.
M-M: Represents the result of a floating-point subtraction (SUB.D).
M-M+M: Represents the result of a floating-point addition (or subtraction) performed on the result of a previous operation.

## Slide 25: Tomasulo Example Cycle 12
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3
Busy Op
No No
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
F0 F2 F4 F6
3 Mult1 Mult2
F8 F10
F12 ... F30
Register result status:
Clock
12
FU Mult1 M(A2) (M-M+M(M-M) Mult2

## Slide 26: Tomasulo Example Cycle 13
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3
Busy Op
No No
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
F0 F2 F4 F6
2 Mult1 Mult2
F8 F10
F12 ... F30
Register result status:
Clock
13
FU Mult1 M(A2) (M-M+M(M-M) Mult2

## Slide 27: Tomasulo Example Cycle 14
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 |  |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3
Busy Op
No No
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
F0 F2 F4 F6
1 Mult1 Mult2
F8 F10
F12 ... F30
Register result status:
Clock
14
FU Mult1 M(A2) (M-M+M(M-M) Mult2

## Slide 28: Tomasulo Example Cycle 15
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 | 15 |  | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3
Busy Op
No No
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
F0 F2 F4 F6
0 Mult1 Mult2
F8 F10 F12
... F30
Register result status:
Clock
15
FU Mult1 M(A2) (M-M+M(M-M) Mult2
Mult1 (MULTD) completing; what is waiting for it?
Notes: Mult1 (MULTD) completing execution
Q. What is waiting for it?
A. Mult2 (DIVD)

## Slide 29: Tomasulo Example Cycle 16
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 | 15 | 16 | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
16 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3 Mult1
Busy Op
40 Mult2
No No
No No
Yes DIVD M*F4 M(A1)
F0 F2 F4
F6 F8 F10 F12 ... F30
Register result status:
Clock
16
FU M*F4 M(A2) (M-M+M(M-M) Mult2
Must wait for Mult2 (DIVD) to complete; skip 39 no-new-action cycles … )
Notes: Now we must wait for Mult2 (DIVD) to complete.
(Skip 39 cycles)
M*F4: books notation (nonstandard)
M: from M(A2)
M*F4: M(A2) multiplied with the value from R(F4)

## Slide 30: … Tomasulo Example Cycle 55
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 | 15 | 16 | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
16 | DIVD | F10 | F0 | F6 | 5 |  |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3 Mult1
Busy Op
1 Mult2
No No
No No
Yes DIVD M*F4 M(A1)
F0 F2 F4
F6 F8 F10
F12 ... F30
Register result status:
Clock
55
FU M*F4 M(A2) (M-M+M(M-M) Mult2

## Slide 31: Tomasulo Example Cycle 56
Instruction status: EX Instruction j |  |  |  | k | Issue | Exec Comp | Write Result | Busy |  | Address
2 | LD | F6 | 34+ | R2 | 1 | 3 | 4 | Load1 | No | 
3 | LD | F2 | 45+ | R3 | 2 | 4 | 5 | Load2 | No | 
5 | MULTD | F0 | F2 | F4 | 3 | 15 | 16 | Load3 | No | 
5 | SUBD | F8 | F6 | F2 | 4 | 7 | 8 |  |  | 
16 | DIVD | F10 | F0 | F6 | 5 | 56 |  |  |  | 
8 | ADDD | F6 | F8 | F2 | 6 | 10 | 11 |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Name Add1 Add2 Add3 Mult1
Busy Op
0 Mult2
No No
No No
Yes DIVD M*F4 M(A1)
F0 F2 F4
F6 F8 F10 F12
... F30
Register result status:
Clock
56
FU M*F4 M(A2) (M-M+M(M-M) Mult2
Mult2 (DIVD) is completing; what is waiting for it?
Notes: Mult2 (DIVD) is completing execution.
Q. What is waiting for it?
A. Nothing

## Slide 32: Tomasulo Example Cycle 57
Instruction status:
Exec Write Issue Comp Result
Busy
Address
1
2
3
4
5
6
3
4
15
7
56
10
4
5
16
8
57
11
Load1 No
Load2 No
Load3 No
ADDD
j k
LD F6 34+ R2
LD F2 45+ R3
MULTD F0 F2 F4 SUBD F8 F6 F2
F10 F0 F6
F6 F8 F2
EX Instruction
Reservation Stations:
S1
Vj
S2
Vk
RS
Qj
RS
Qk
Time
Busy Op
Name
Add1 No
Add2 No
Add3 No
Mult1 No
Mult2 Yes
DIVD
M*F4
M(A1)
Register result status:
Clock
56
... F30
F0 F2 F4 F6 F8 F10 F12
FU M*F4 M(A2) (M-M+M(M-M) Result
2
3
5
5
16 DIVD
8
Once again: In-order issue, out-of-order start of execution, and out-of-order completion.
Notes: >>
Reiteration of the key performance sequence:
In-order issue,
out-of-order start of execution,
and out-of-order completion.

## Slide 33: Tomasulo’s Scheme: Two Major Advantages
Distribution of the hazard detection logic
  Distributed reservation stations and the CDB
  If multiple instructions are waiting on a single result and each instruction has its other operand, then instructions can be released simultaneously by result being broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available (slower)
Elimination of stalls for WAW and WAR hazards
Notes: >>
Two major advantages to Tomasulo:
Distribution of hazard detection logic: CDB broadcasts results simultaneously, thereby releasing multiple waiting instructions. (arrow down)
It will eliminate all WAW and WAR stalls.

## Slide 34: Tomasulo Drawbacks
Complexity
– Delays of 360/91, MIPS 10000, Alpha 21264,
IBM PPC 620 (in CA:AQA 2/e, before it was in silicon!)
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units
 high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
» Multiple CDBs  more FU logic for parallel associative stores
Non-precise exception handling!
Notes: >>
Disadvantages to Tomasulo:
High complexity. (arrow down)
Performance is limited by the single CDB; requires multiple CDBs to support more parallel completion. (arrow down)
Non-precise exception handling is a major issue.

## Slide 35: Why Can Tomasulo Overlap Iterations Of Loops?
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall
Other perspective:
Tomasulo hardware builds data flow dependency graphs on the fly
Notes: >>
Q. Why can Tomasulo overlap iterations of a loop?
A.
Register Renaming allows multiple iterations to use different physical registers, enabling dynamic loop unrolling.
(arrow down)
Reservation Stations buffer old register values, totally avoiding the WAR stall.
(arrow down)
…

## Slide 36: Tomasulo Loop Example
Loop: | LD MULTD | F0 F4 | 0 F0 | R1 F2
 | SD | F4 | 0 | R1
 | SUBI | R1 | R1 | #8
 | BNEZ | R1 | Loop | 
Assume multiply takes 4 clock cycles
Assume first load takes 8 clock cycles (cache miss?), second load takes 4 clock cycles (hit)
To be clear, SUBI, BNEZ will not be explicitly shown but still need to account for their clock cycles
Notes: >>
Here is a step-by-step example showing how
Tomasulo's hardware dynamically overlaps iterations of a loop for increased performance.
(Go over the example code and assumptions.)

## Slide 37: Loop Example Cycle 0
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 |  |  |  | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 |  |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 |  |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 |  |  |  | Store1 | No |  |  | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | No |  |  |  |  |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
0 |  | 80 | Qi |  |  |  |  |  |  |  |  | 

## Slide 38: Loop Example Cycle 1
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 |  |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 |  |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 |  |  |  | Store1 | No |  |  | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | No |  |  |  |  |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
1 |  | 80 | Qi | Load1 |  |  |  |  |  |  |  | 

## Slide 39: Loop Example Cycle 2
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 |  |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 |  |  |  | Store1 | No |  |  | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
2 |  | 80 | Qi | Load1 |  | Mult1 |  |  |  |  |  | 

## Slide 40: Loop Example Cycle 3
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 |  |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
3 |  | 80 | Qi | Load1 |  | Mult1 |  |  |  |  |  | 
Note: MULT1 has no register names in RS
Notes: Note:
MULT1 has no register names in RS
R(F2) refers to the value of FP register F2

## Slide 41: Loop Example Cycle 4
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 |  |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
4 |  | 72 | Qi | Load1 |  | Mult1 |  |  |  |  |  | 

## Slide 42: Loop Example Cycle 5
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 |  |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
5 |  | 72 | Qi | Load1 |  | Mult1 |  |  |  |  |  | 

## Slide 43: Loop Example Cycle 6
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | Yes | 72 |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 | 6 |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 |  |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
6 |  | 72 | Qi | Load2 |  | Mult1 |  |  |  |  |  | 
Note: F0 never sees Load1 result
Notes: Note:
F0 never sees Load1 result
This is because the instruction for Load2 will also be writing to the CDB for F0.

## Slide 44: Loop Example Cycle 7
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | Yes | 72 |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 | 6 |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 |  |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | Yes | MULTD |  | R(F2) | Load2 |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
7 |  | 72 | Qi | Load2 |  | Mult2 |  |  |  |  |  | 
Note: MULT2 has no registers names in RS
Notes: Note:
MULT2 has no registers names in RS

## Slide 45: Loop Example Cycle 8
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 |  |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | Yes | 72 |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 | 6 |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | Yes | MULTD |  | R(F2) | Load2 |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
8 |  | 72 | Qi | Load2 |  | Mult2 |  |  |  |  |  | 

## Slide 46: Loop Example Cycle 9
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 |  | Load1 | Yes | 80 |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | Yes | 72 |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 | 6 |  |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load1 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | Yes | MULTD |  | R(F2) | Load2 |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
9 |  | 64 | Qi | Load2 |  | Mult2 |  |  |  |  |  | 
Load1 completing; what is waiting for it?
Notes: Load1 completing execution
(EX 2-9 for 1st load: 8 cycles)
Q. What is waiting for it?
A. Mult1 (MUL.D)

## Slide 47: Loop Example Cycle 10
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | Yes | 72 |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | No |  | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 |  | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 4 | Mult1 | Yes | MULTD | M(80) | R(F2) |  |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | Yes | MULTD |  | R(F2) | Load2 |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
10 |  | 64 | Qi | Load2 |  | Mult2 |  |  |  |  |  | 
Load2 completing; what is waiting for it?

## Slide 48: Loop Example Cycle 11
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 3 | Mult1 | Yes | MULTD | M(80) | R(F2) |  |  | SUBI | R1 | R1 | #8
 | 4 | Mult2 | Yes | MULTD | M(72) | R(F2) |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
11 |  | 64 | Qi | Load3 |  | Mult2 |  |  |  |  |  | 
Notes: L.D in 3rd iteration is now issued, uses Load3 RS.

## Slide 49: Loop Example Cycle 12
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 2 | Mult1 | Yes | MULTD | M(80) | R(F2) |  |  | SUBI | R1 | R1 | #8
 | 3 | Mult2 | Yes | MULTD | M(72) | R(F2) |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
12 |  | 64 | Qi | Load3 |  | Mult2 |  |  |  |  |  | 
MULT in 3rd iteration cannot be issued
Notes: MULTD in 3rd iteration cannot be issued (structural: not enough FP multiply FUs)

## Slide 50: Loop Example Cycle 13
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 |  |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 1 | Mult1 | Yes | MULTD | M(80) | R(F2) |  |  | SUBI | R1 | R1 | #8
 | 2 | Mult2 | Yes | MULTD | M(72) | R(F2) |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
13 |  | 64 | Qi | Load3 |  | Mult2 |  |  |  |  |  | 

## Slide 51: Loop Example Cycle 14
• Mult1 completing; what is waiting for it?
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 | 14 |  | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 |  |  | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | Yes | 80 | Mult1 | 
MULT | F4 | F0 | F2 | 2 | 7 |  |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD | M(80) | R(F2) |  |  | SUBI | R1 | R1 | #8
 | 1 | Mult2 | Yes | MULTD | M(72) | R(F2) |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
14 |  | 64 | Qi | Load3 |  | Mult2 |  |  |  |  |  | 
Notes: Mult1 completing execution.
(EX 11-14 due to Load1 WR CDB in 10 for RAW on F0, Also multiply EX is 4 cycles)
Q. What is waiting for it?
A. Store1 (SD)

## Slide 52: Loop Example Cycle 15
• Mult2 completing; what is waiting for it?
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 | 14 | 15 | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 | 15 |  | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | Yes | 80 | M(80)*R(F | 
MULT | F4 | F0 | F2 | 2 | 7 | 15 |  | Store2 | Yes | 72 | Mult2 | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | No |  |  |  |  |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | Yes | MULTD | M(72) | R(F2) |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
15 |  | 64 | Qi | Load3 |  | Mult2 |  |  |  |  |  | 
Notes: Mult2 completing execution.
(EX 12-15 due to Load2 WR CDB in 11 for RAW on F0, Also multiply EX is 4 cycles)
Q. What is waiting for it?
A. Store2 (SD)

## Slide 53: Loop Example Cycle 16
• MULT in 3rd iteration is now issued
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 | 14 | 15 | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 | 15 | 16 | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | No |  |  | 
MULT | F4 | F0 | F2 | 2 | 7 | 15 |  | Store2 | Yes | 72 | M(72)*R(F | 
SD | F4 | 0 | R1 | 2 | 8 |  |  | Store3 | No |  |  | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load3 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | Yes | MULTD | M(72) | R(F2) |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
16 |  | 64 | Qi | Load3 |  | Mult1 |  |  |  |  |  | 
Notes: MULTD in 3rd iteration is now issued

## Slide 54: Loop Example Cycle 17
• SD in 3rd iteration is now issued
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 | 14 | 15 | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 | 15 | 16 | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | No |  |  | 
MULT | F4 | F0 | F2 | 2 | 7 | 15 | 17 | Store2 | Yes | 72 | M(72)*R(F | 
SD | F4 | 0 | R1 | 2 | 8 | 17 |  | Store3 | Yes | 64 | Mult1 | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load3 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
17 |  | 64 | Qi | Load3 |  | Mult1 |  |  |  |  |  | 
Notes: SD in 3rd iteration is now issued

## Slide 55: Loop Example Cycle 18
Instruction status |  |  |  |  |  | Execution | Write |  |  |  |  | 
Instruction |  | j | k | iteration | Issue | complete | Result |  | Busy | Address |  | 
LD | F0 | 0 | R1 | 1 | 1 | 9 | 10 | Load1 | No |  |  | 
MULT | F4 | F0 | F2 | 1 | 2 | 14 | 15 | Load2 | No |  |  | 
SD | F4 | 0 | R1 | 1 | 3 | 15 | 16 | Load3 | Yes | 64 | Qi | 
LD | F0 | 0 | R1 | 2 | 6 | 10 | 11 | Store1 | No |  |  | 
MULT | F4 | F0 | F2 | 2 | 7 | 15 | 17 | Store2 | No |  |  | 
SD | F4 | 0 | R1 | 2 | 8 | 17 | 18 | Store3 | Yes | 64 | Mult1 | 
Reservation Stations |  |  |  |  | S1 | S2 | RS for j | RS for k |  |  |  | 
 | Time | Name | Busy | Op | Vj | Vk | Qj | Qk | Code: |  |  | 
 | 0 | Add1 | No |  |  |  |  |  | LD | F0 | 0 | R1
 | 0 | Add2 | No |  |  |  |  |  | MULT | F4 | F0 | F2
 | 0 | Add3 | No |  |  |  |  |  | SD | F4 | 0 | R1
 | 0 | Mult1 | Yes | MULTD |  | R(F2) | Load3 |  | SUBI | R1 | R1 | #8
 | 0 | Mult2 | No |  |  |  |  |  | BNEZ | R1 | Loop | 
Register result status |  |  |  |  |  |  |  |  |  |  |  | 
Clock |  | R1 |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 | ... | F30
18 |  | 56 | Qi | Load3 |  | Mult1 |  |  |  |  |  | 
Once again: In-order issue, out-of-order start of execution, and out-of-order completion
Notes: >>
Reiteration of the key performance sequence:
In-order issue,
out-of-order start of execution,
and out-of-order completion.

## Slide 56: And In Conclusion … #1
Leverage Implicit Parallelism for Performance: Instruction Level Parallelism
Loop unrolling by compiler to increase ILP
Branch prediction to increase ILP
Dynamic HW exploiting ILP
  Works when cannot know dependences at compile time
  Can hide L1 cache misses
  Code for one pipelined machine runs well on another
Notes: >>
Instruction-Level Parallelism (ILP)
enhances processor performance
by enabling the execution of multiple instructions
simultaneously within a single instruction stream.
(arrow down)
Loop unrolling and branch prediction
increase simultaneous execution of instructions.
(arrow down)
Dynamic hardware exploits Instruction Level Parallelism to
Discover data dependences that are only known dynamically (during runtime) (such as when they involve memory references)
Enables the processor to hide stalls caused by L1 cache misses by continuing to execute other available instructions while waiting for the required data
Because the hardware manages scheduling and dependences at runtime, code compiled for one pipelined processor can run efficiently on different pipeline implementations without requiring recompilation, enhancing code portability.

## Slide 57: And In Conclusion … #2
Reservations stations: renaming to larger set of registers + buffering source operands
  Prevents registers from being bottlenecks
  Avoids WAR, WAW hazards
  Allows dynamic loop unrolling in hardware
Not limited to basic blocks
(integer units get ahead, beyond branches)
Helps cache misses as well
Lasting Contributions of Tomasulo
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Intel Pentium 4, IBM Power 5, AMD Athlon/Opteron, …
Notes: >>
Reservation stations enable renaming to a larger set of "registers" and buffer source operands,
preventing registers from being a bottleneck.
Difference between Tomasulo and Scoreboard:
Tomasulo's algorithm eliminates data hazards,
including Write-After-Write (WAW)
and Write-After-Read (WAR) hazards,
primarily through the use of register renaming
implemented via reservation stations.
The scoreboard method does not inherently eliminate WAW and WAR hazards.
It relies on stalling the pipeline when such hazards are detected
(particularly at the issue stage) to maintain program order.
While the scoreboard can handle Read-After-Write (RAW) hazards
through result forwarding and operand availability checks,
it lacks a mechanism like register renaming to resolve name dependencies.
(arrow down)
Supports speculative execution for dynamic branch predictions.
(arrow down)
Tomasulo's algorithm enhances tolerance for cache misses
by enabling the processor to continue executing other instructions
while waiting for data from memory.
(thus, maintaining concurrency during unpredictable load times)
(arrow down)
Descendants still exist in modern CPUs.