## Slide 1
Chapter 3 and Appendix C
Tomasulo with Speculation
Computer Architecture
A Quantitative Approach

## Slide 2: ADDING SPECULATION TO TOMASULO’S ALGORITHM
2

## Slide 3: Speculation For Greater ILP
In Tomasulo, to preserve exception behavior, no instruction is allowed to initiate execution until all preceding branches have completed.
Greater ILP: Overcome control dependence by hardware speculating on outcome of branches and executing program as if guesses were correct
  Speculation  fetch, issue, and execute instructions as if branch predictions were always correct
  Dynamic scheduling  only fetches and issues instructions
Essentially, a data flow execution model: Operations execute as soon as their operands are available
Notes: Standard Tomasulo prevents execution until preceding branches resolve (for precise exceptions).
Speculation overcomes control dependence by predicting branches and executing instructions out-of-order.
This creates a data flow execution model.

## Slide 4
Three components of HW-based speculation:
Dynamic branch prediction to choose which instructions to execute
Speculation to allow execution of instructions before control dependences are resolved
– + Ability to undo effects of incorrectly speculated sequence
Dynamic scheduling to deal with scheduling of combinations of basic blocks revealed at runtime
speculatively executing post-branch instructions
Speculation For Greater ILP
Notes: Three components of HW-based speculation:
Dynamic branch prediction to guide instruction fetching.
Speculation allowing execution before control dependence is resolved.
Ability to undo effects of incorrect speculation (misprediction).

## Slide 5: Adding Speculation to Tomasulo
Must separate execution from allowing instruction to finish or “commit”
  This additional step is called instruction commit; it occurs whenever the branch prediction is confirmed for the branch immediately before a block of speculated instructions.
When an instruction is no longer speculative, allow it to update the register file or memory.
Requires an additional set of buffers to hold results of instructions that have finished execution but have not committed.
  This reorder buffer (ROB) is also used to pass results among instructions that may be speculated.
Notes: Introduces the commit stage to separate instruction execution from completion/finish.
An instruction commits only after its preceding branch prediction is confirmed.
The Reorder Buffer (ROB) holds results of executed but uncommitted instructions.

## Slide 6: Reorder Buffer (ROB)
In Tomasulo’s algorithm, once an instruction writes its result, any subsequently issued instructions will find result in the register file
With speculation, the register file is not updated until the instruction commits
  (i.e., when we know for sure that the instruction should have executed)
The ROB supplies operands in the interval between completion of instruction execution and instruction commit
  ROB is a source of operands for instructions, just as reservation stations (RS) provide operands in Tomasulo’s algorithm
  ROB extends architectured registers as the reservation stations did
Notes: The Register File is not updated until an instruction commits.
The ROB supplies results (operands) between execution completion and commit.
The ROB is an extension of architected registers, similar to Reservation Stations (RS).

## Slide 7: Reorder Buffer Entry Fields
Each entry in the ROB contains four fields:
Instruction type
  A branch (has no destination result), a store (has a memory address destination), or a register operation (ALU operation or load, each of which has a register destination for writeback)
Destination
  Register number (for loads and ALU operations) or memory address (for stores) - where the instruction result should be written
Value
  Value of instruction result being held until the instruction commits
Ready
  Indicates that instruction has completed execution, and the value is ready once the instruction commits
Notes: Each ROB entry contains four fields:
Instruction Type (Branch, Store, or Register Op),
Destination (Register or Memory Address),
Value (Result held until commit), and
Ready (Indicates execution is complete).

## Slide 8: Reorder Buffer Operation
Holds instructions in FIFO order, exactly as issued
When instructions complete, results placed into ROB
  Supplies operands to other instruction between execution complete & commit  more registers like RSs (reservation stations)
  Tag results with ROB buffer number instead of RS number
Instructions commit values at head of ROB placed in
registers (or memory)
As a result, easy to undo speculated instructions on mispredicted branches or on exceptions
Commit path from head of buffer
Reorder Buffer
FP
Op
Queue
FP Adder
FP M’plier
Res Stations
Res Stations
FP Regs
Notes: Instructions are held in FIFO (in-order) issue order.
Commit (writing to registers/memory) occurs in order from the head of the ROB.
This FIFO commit allows easy recovery from mispredictions/exceptions.

## Slide 9: 4 Steps of Speculative Tomasulo Algorithm
Issue—get instruction from FP Op Queue
  If RS and ROB slot free, issue instruction & send the operands to RS if available in registers or ROB, and send ROB no. for destination to RS (this stage sometimes called “dispatch”)
Execution—operate on operands (EX)
  Checks for RAW hazards; when both operands ready then execute; if not ready, watch CDB for result; when both in RS, execute (sometimes called “issue”)
Write result—finish execution (WB)
  Write on CDB to all awaiting FUs & reorder buffer; mark RS available.
Commit—update register with reorder result
  When instruction at head of reorder buffer & result are present and the branch before it has been confirmed, update register with result (or store to memory) and remove instruction from ROB. Mispredicted branch flushes ROB above (executed after) the branch (sometimes called “graduation”)
(steps added for speculation in blue)
Notes: 4 Steps of Speculative Tomasulo Algorithm
Issue: (Dispatch) Get instruction; If RS and ROB slot free, issue. Send ROB number as destination tag to RS.
Execution: (EX/Issue) Operates on operands.
Write Result: (WB) Write result to CDB and ROB.
Commit: (Graduation) Instruction at ROB head updates register/memory in-order and is removed. Mispredicted branches flush the ROB of executed instructions after the branch.

## Slide 10: Tomasulo With Reorder buffer:
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
0(R3),F4
Dest. Value Instruction
Notes: Step-by-step example execution showing instruction flow through
Reservation Stations (RS),
the Reorder Buffer (ROB),
and the Register Status table.

## Slide 11: Tomasulo With Reorder buffer:
2
ADDD
R(F4), ROB1
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
0(R3),F4
Dest. Value Instruction

## Slide 12: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
2
ADDD
R(F4), ROB1
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
0(R3),F4
Dest. Value Instruction

## Slide 13: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
R(F4), ROB1
ROB5, R(F6)
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4, 0(R3)
N
--
BNE F2, <…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
5
0+R3
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
2 ADDD
6 ADDD
0(R3),F4
Dest. Value Instruction

## Slide 14: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
R(F4), ROB1
ROB5, R(F6)
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
--
F0
ROB5
ST 0(R3), F4
ADDD F0,F4,F6
N
N
F4
LD F4, 0(R3)
N
--
BNE F2, <…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
5
0+R3
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
2 ADDD
6 ADDD
0(R3),F4
Dest. Value Instruction

## Slide 15: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
R(F4), ROB1
M[10], R(F6)
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
--
F0
M[10]
ST 0(R3), F4
ADDD F0,F4,F6
Y
N
F4
M[10]
LD F4, 0(R3)
Y
--
BNE F2, <…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
2 ADDD
6 ADDD
0(R3),F4
Dest. Value Instruction

## Slide 16: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
2
ADDD
R(F4), ROB1
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
--
F0
M[10]
<val2>
ST 0(R3), F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4, 0(R3)
Y
--
BNE F2, <…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6
DesStT
0(R3),F4
Dest. Value Instruction

## Slide 17: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
2
ADDD
R(F4), ROB1
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
F4 M[10]
LD F4, 0(R3)
ROB7 ROB6
Y ROB5 ROB4
ROB3 ROB2 ROB1
--
BNE F2, <…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
LD F0,10(R2) ADDD F10,F4,F0 DIVD F2,F10,F6 BNE F2,<…>
LD F4,0(R3) ADDD F0,F4,F6 ST 0(R3),F4
Dest. Value Instruction

## Slide 18: Tomasulo With Reorder buffer:
3
DIVD
ROB2, R(F6)
2
ADDD
R(F4), ROB1
FP adders
FP multipliers
Reservation Stations
FP Op
Queue
ROB7 ROB6
ROB5 ROB4 ROB3 ROB2 ROB1
F4 M[10]
LD F4, 0(R3)
Y
--
BNE F2, <…>
N
F2 F10 F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
To Memory
from Memory
1
10+R2
Dest
ROB
Registers
Dest. Value Instruction
What about memory
hazards???
Notes: What about memory hazards???
(next slide)

## Slide 19: Avoiding Memory Hazards
WAW and WAR hazards through memory are eliminated with speculation because actual updating of memory occurs in order, when a store is at head of the ROB, and hence, no earlier loads or stores can still be pending
RAW hazards through memory are avoided by two restrictions:
  not allowing a load to initiate the second step (actual memory read) of its execution if any active ROB entry occupied by a store has a Destination field that matches the value of the Addr. field of the load, and
  maintaining the program order for the computation of an effective address of a load with respect to all earlier stores.
These restrictions ensure that any load that accesses a memory location written to by an earlier store cannot perform the memory access until the store has written the data
Notes: WAW/WAR hazards through memory are eliminated because Stores only update memory when they reach the ROB head (in-order completion).
RAW hazards (Load-after-Store) are avoided by checking if an earlier active store in the ROB has a matching address before allowing a load to read memory.

## Slide 20: Exceptions and Interrupts
IBM 360/91 invented “imprecise interrupts”
  “Computer stopped at this PC; error likely near this address”
  Not so popular with programmers
Technique for both precise interrupts/exceptions and speculation: in-order completion and in-order commit
  If we speculate and are wrong, need to back up and restart execution to point at which we predicted incorrectly
  Exactly the same must be done for precise exceptions
Exceptions are handled by not recognizing the exception until instruction that caused it is ready to commit in ROB
  If a speculated instruction raises an exception, the exception is recorded in the ROB
  There are reorder buffers in all new processors to provide precise interrupts, which help programmers find errors faster.
Notes: Speculation requires in-order commit to support precise exceptions.
If a speculated instruction causes an exception,
it is recorded in the ROB but not recognized until the instruction is ready to commit (at the ROB head).
The ROB enables precise exception handling in modern processors.